| Fire Extinguishers Annual Service Due: |
| --- |
| Location | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec |

| Emergency Lights |
| --- |
| Location | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec |

| Smoke / Fire Detectors Annual System Service Due: |
| --- |
| Location | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec |

| Eye Wash Stations |
| --- |
| Location | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec |

Instructions

Fire Extinguishers should be visually checked to ensure:

C	they are still in place and properly mounted;

C	the pressure indicator dial (if equipped) is in the green or charged area;

C	the pull pin is in place and fastened with the security seal

C	the body of the extinguisher is free from dents, cracks, corrosion or leaks;

C	the hose (if equipped) is intact and free from obstructions; and

C	the test button (if equipped) operates properly.

Emergency Lights should:

C	be tested by depressing the test button or disrupting the electrical current to the device.  Units without a test button can be unplugged or the circuit breaker servicing that circuit can be turned off;

C	immediately come on and light all bulbs in the device; and

C	be focused or directed so that they illuminate the way to the exit.

Smoke / Fire Detectors should be:

C	checked to ensure they are still in place, properly mounted and free from obvious damage;

C	tested by depressing the test button until the alarm sounds (see note below for centrally-monitored systems).

NOTE: for centrally-monitored alarm systems, follow the procedures outlined in the system manufacturer’s literature.  Always notify the monitoring system and/or fire department that you are about to conduct an alarm test of the system.

Eyewash Stations should be examined to ensure:

C	the unit is in place and free from obvious damage;

C	the device is positioned so that a person’s head can be positioned in the water flow without restrictions from other objects;

C	the outlet ports are free from obstructions and the protective caps are in place;

C	the outlet ports are positioned so that both eyes are flushed simultaneously;

C	the protective caps are released when the unit activates and does not require additional steps; and

C	the unit operates properly for at least 15 minutes.